## Slide 1: 2021 CAD Contest @ ICCAD Macro Legalization
National Taiwan University of Science and Technology
YU-CHE LEE

## Slide 2
Problem：Macro Legalization
Mixed-size Prototyping
Macro Placement
Standard-cell Placement

## Slide 3: Problem Statement
Design Rules
  Non-overlapping constraint
  Fixed-outline constraint
  Min. channel spacing constraint
  Buffer area reservation constraint
Objective Function
  Minimize total displacement
    Small disturbance
  Minimize dead space
    More space for standard cell
Within 15 minutes

## Slide 4: Algorithm Flow Chart

## Slide 5: Step 1 - Preprocessing

## Slide 6: Make Chip Boundary Rectangular
Use sweep-line algorithm to fill up notches with pre-placed macros.
Find bounding box
Chip boundary
Fill up with pre-placed macro

## Slide 7: Move Macro Into Boundary
Move the macro which violates fixed-outline constraint inside the nearest boundary.

## Slide 8: Step 2 - Overlap Reduction

## Slide 9: Force-directed-like Algorithm
  Repulsive force are applied within macros to globally reduce overlap.
  where Area is the size of macro, and O is the min{Width, Height of overlapped
  region}

## Slide 10: Overlap Reduction Example
Simple case can be handled easily
Before reduce overlap
After reduce overlap

## Slide 11: Step 3 - Global Legalization

## Slide 12: Build Constraint Graph
  According to the placement, build the horizontal and vertical constraint graph(CG).
Horizontal CG
Vertical CG
Placement
: Macro
: Edge, ω is edge weight, representing the non-overlapping constraint of two end-points
ω

## Slide 13: Check Critical Path
  Check if the critical path of CG is longer than the chip size
    If yes, remove the smallest macro in the critical path
…
Critical path
Removed smallest macro

## Slide 14: Linear Programming Formulation
Transform both CGs into linear inequality as constraint
Take minimal displacement as the objective function
Horizontal CG
Vertical CG
s.t.

## Slide 15: Remove Overlap - Before
Linear programming solver removes overlap with minimal displacement
Before remove overlap
Macro Removed macro

## Slide 16: Remove Overlap - After
Linear programming solver removes overlap with minimal displacement
Macro Removed macro
After remove overlap

## Slide 17: Step 4 - Dead Space Optimization

## Slide 18: Dead Space Optimization
Expand two adjacent macros’ distance, trying to turn dead space into free space
Dead space
Free space
Non-overlapping constraint
Non-overlapping constraint +=
Power_plane_constraint
1
2
3

## Slide 19: Dead Space Optimization - Example
Before Dead Space Optimization
After Dead Space Optimization
Macro
Dead Space
Reduce 39.14% dead space

## Slide 20: Step 5 - Detail Legalization

## Slide 21: Corner Stitching Structure
Empty space is represented explicitly
Rectangular objects are stitched together at their corners

## Slide 22: Corner Stitching Structure - Example
Before empty space is represented

## Slide 23: Corner Stitching Structure - Example
After empty space is represented

## Slide 24: Search Area Using Corner Stitching
Linear time for searching empty area surrounding the macro

## Slide 25: Detail Legalization - Example
Place the illegal macro into the nearest empty space by using corner stitching

## Slide 26: Step 6 - Buffer Area Reservation Constraint Legalization

## Slide 27: Buffer Area Reservation Constraint Intro.
Every extended distance from the macro must cover free space
Legal
Illegal

## Slide 28: Spread Along One Direction
Find the least crowed direction
Illegal macro
Legal macro

## Slide 29: Spread Along One Direction
Find the least crowed direction
Push macro which belongs to that direction away
Illegal macro
Legal macro

## Slide 30: Dummy Point Insertion Intro.
Dummy point is a minimal rectangle to represent a std. cell
Every extended distance from the macro must cover free space
≡
Every extended distance from the macro must cover a dummy point

## Slide 31: Dummy Point Insertion - Example
Macro
Dummy point

## Slide 32: Experimental Result
Benchmark (Synopsys, Inc.) | Total displacement (micron) | Free space (micron^2) | Ranking
Industrial 1 | 2130 | 66593 | 2/21
Industrial 2 | 28093 | 114488 | 5/21
Industrial 3 | 21521 | 383400 | 2/21
Industrial 4 | 2303 | 43287 | 3/21
Industrial 5 | 2381 | 92627 | 3/21
Industrial 6 | 12632 | 245548 | 2/21
Industrial 7 | 3295 | 106870 | 4/21
Industrial 8 | 5001 | 111967 | 3/21
Industrial 9 | 15214 | 557947 | 1/21
Industrial 10 | 11362 | 408946 | 1/21

## Slide 33: Final Example – Industrial 3
Initial placement violates the design rules

## Slide 34: Final Example – Industrial 3
Placement after running the macro legalization

## Slide 35: Final Example – Industrial 5
Initial placement violates the design rules

## Slide 36: Final Example – Industrial 5
Placement after running the macro legalization

## Slide 37: Final Example – Industrial 6
Initial placement violates the design rules

## Slide 38: Final Example – Industrial 6
Placement after running the macro legalization

## Slide 39: Final Example – High Density Case
Initial placement violates the design rules

## Slide 40: Final Example – High Density Case
Placement after running the macro legalization